ROS - Lesson 5
Teaching Assistant: Roi Yehoshua
roiyeho@gmail.com

---
Agenda
Agenda
- Understanding costmaps
- move_base package
- Running ROS navigation in Stage
- Using rviz with navigation stack

---
Navigation Stack
Navigation Stack

---
Costmap
Costmap
- The costmap is the data structure that represents places that are safe for the robot to be in a grid of cells
- Usually, the values in the costmap are binary, representing free space or places where the robot would be in collision.

---
Costmap Types
Costmap Types
- Our robot will move through the map using two types of navigation—global and local.
- The global navigation is used to create paths for a goal in the map or a far-off distance
  - The global costmap is used for the global navigation
- The local navigation is used to create paths in the nearby distances and avoid obstacles
  - The local costmap is used for the local navigation

---
costmap_2d Package
costmap_2d Package
- http://wiki.ros.org/costmap_2d
- The costmap_2d package uses sensor data and information from the static map to build a 2D or 3D occupancy grid of the data and inflate costs in a 2D costmap based on the occupancy grid and a user specified inflation radius.

---
Costmap Example
Costmap Example

---
Costmap Values
Costmap Values
- Each cell in the costmap has a value in the range [0, 255] (integers).
- There are some special values frequently used in this range. (defined in include/costmap_2d/cost_values.h)
  - costmap_2d::NO_INFORMATION (255) - Reserved for cells where not enough information is sufficiently known.
  - costmap_2d::LETHAL_OBSTACLE (254) - Indicates a collision causing obstacle was sensed in this cell.
  - costmap_2d::INSCRIBED_INFLATED_OBSTACLE (253) - Indicates no obstacle, but moving the center of the robot to this location will result in a collision.
  - costmap_2d::FREE_SPACE (0) - Cells where there are no obstacles and the moving the center of the robot to this position will not result in a collision.

---
Map Types
Map Types
There are two main ways to initialize a costmap:
Seed it with a user-generated static map
  1. In this case, the costmap is initialized to match the width, height, and obstacle information provided by the static map.
  2. This configuration is normally used in conjunction with a localization system, like amcl, that allows the robot to register obstacles in the map frame and update its costmap from sensor data as it drives through its environment.

---
Map Types
Map Types
Define a width and height and set the rolling_window parameter to be true.
  1. The rolling_window parameter keeps the robot in the center of the costmap as it moves throughout the world, dropping obstacle information from the map as the robot moves too far from a given area.
  2. This type of configuration is most often used in an odometric coordinate frame where the robot only cares about obstacles within a local area.

---
Map Updates
Map Updates
- The costmap performs map update cycles at the rate specified by the update_frequency parameter.
- In each cycle:
  - sensor data comes in
  - marking and clearing operations are perfomed in the underlying occupancy structure of the costmap
  - this structure is projected into the costmap where the appropriate cost values are assigned as described above.
  - obstacle inflation is performed on each cell with a costmap_2d::LETHAL_OBSTACLE. This consists of propagating cost values outwards from each occupied cell out to a user-specified inflation radius.

---
Marking and Clearing
Marking and Clearing
- Each sensor is used to either mark (insert obstacle information into the costmap), clear (remove obstacle information from the costmap), or both.
- A marking operation is just an index into an array to change the cost of a cell.
- A clearing operation, however, consists of raytracing through a grid from the origin of the sensor outwards for each observation reported.

---
Inflation
Inflation
- Inflation is the process of propagating cost values out from occupied cells that decrease with distance.
- For this purpose, there are 5 specific symbols defined for costmap values:
  - "Lethal" cost means that there is an actual obstacle in a cell. So if the robot's center were in that cell, the robot would obviously be in collision.
  - "Inscribed" cost means that a cell is less than the robot's inscribed radius away from an obstacle. So the robot is certainly in collision with an obstacle if the robot center is in a cell that is at or above the inscribed cost.

---
Inflation
Inflation
  - "Possibly circumscribed“ cost is similar to inscribed, but using the robot's circumscribed radius as cutoff distance. Thus, if the robot center lies in a cell at or above this value, then it depends on the orientation of the robot whether it collides with an obstacle or not.
    - In addition, it might be that it is not really an obstacle cell, but some user-preference, that put that particular cost value into the map.
    - For example, if a user wants to express that a robot should attempt to avoid a particular area of a building, they may inset their own costs into the costmap for that region independent of any obstacles.

---
Inflation
Inflation
  - "Freespace" cost is assumed to be zero, and it means that there is nothing that should keep the robot from going there.
  - "Unknown" cost means there is no information about a given cell. The user of the costmap can interpret this as they see fit.
All other costs are assigned a value between "Freespace" and "Possibly circumscribed" depending on their distance from a "Lethal" cell and the decay function provided by the user.

---
Inflation
Inflation

---
Costmap Layers
Costmap Layers
- In ROS Hydro, a new layered structure was created for costmap.
- The static map, the sensed obstacles and the inflated areas are separated into distinct layers.
- Users can specify additional layers using ROS plugins
  - For example, you can integrate a special "social" costmap plugin, where the values around sensed people is increased proportional to a normal distribution, causing the robot to tend to drive further away from the person.
- Tutorial for creating a new costmap layer

---
Costmap2D Class Hierarchy
Costmap2D Class Hierarchy
costmap_2d.h header file:
http://docs.ros.org/electric/api/costmap_2d/html/costmap__2d_8h_source.html

---
Costmap2DROS
Costmap2DROS
- The costmap_2d::Costmap2DROS object is a wrapper for a costmap_2d::Costmap2D object which contains the costmap
- Example creation of a costmap_2d::Costmap2DROS object:
For C++ level API documentation on this class see  Costmap2DROS C++ API

---
Costmap Parameters Files
Costmap Parameters Files
Configuration of the costmaps consists of three files where we can set up different parameters:
  - costmap_common_params.yaml
  - global_costmap_params.yaml
  - local_costmap_params.yaml

---
Global Costmap Parameters
Global Costmap Parameters
Default	Description	Parameter
2.5	The default maximum distance from the robot at which an obstacle will be inserted into the cost map in meters.	obstacle_range
2.0	The maximum height of any obstacle to be inserted into the costmap in meters. This parameter should be set to be slightly higher than the height of your robot.	max_obstacle_height
3.0	The default range in meters at which to raytrace out obstacles from the map using sensor data.	raytrace_range
10.0	A scaling factor to apply to cost values during inflation, according to the formula: / exp(-1.0 * cost_scaling_factor * (distance_from_obstacle – inscribed_radius)) * (costmap_2d::INSCRIBED_INFLATED_OBSTACLE - 1)	cost_scaling_factor

---
Robot Description Parameters
Robot Description Parameters
Default	Description	Parameter
[]	The footprint of the robot specified in the robot_base_frame coordinate frame as a list in the format: [ [x1, y1], [x2, y2], ...., [xn, yn] ]. / The footprint specification assumes the center point of the robot is at (0.0, 0.0) in the robot_base_frame and that the points are specified in meters, both clockwise and counter-clockwise orderings of points are supported.	footprint
0.55	The radius in meters to which the map inflates obstacle cost values	inflation_radius

---
Coordinate Frame Parameters
Coordinate Frame Parameters
Default	Description	Parameter
"/map"	The global frame for the costmap to operate in	global_frame
"base_link"	The name of the frame for the base link of the robot	robot_base_frame
0.2	Specifies the delay in transform (tf) data that is tolerable in seconds. / This parameter serves as a safeguard to losing a link in the tf tree while still allowing an amount of latency the user is comfortable with to exist in the system.	transform_tolerance

---
Rate Parameters
Rate Parameters
Default	Description	Parameter
5.0	The frequency in Hz for the map to be updated	update_frequency
0.0	The frequency in Hz for the map to be publish display information	publish_frequency

---
Sensor Management Parameters
Sensor Management Parameters
Default	Description	Parameter
""	A list of observation source names separated by spaces. This defines each of the <source_name> namespaces defined below.	observation_sources
source_name	The topic on which sensor data comes in for this source. Defaults to the name of the source.	<source_name>/topic
"PointCloud"	The data type associated with the topic, right now only "PointCloud", "PointCloud2", and "LaserScan" are supported.	<source_name>/data_type
0.0	How often to expect a reading from a sensor in seconds. This parameter is used as a failsafe to keep the navigation stack from commanding the robot when a sensor has failed. It should be set to a value that is slightly more permissive than the actual rate of the sensor.	<source_name>/expected_update_rate
false	Whether or not this observation should be used to clear out freespace	<source_name>/clearing

---
Sensor Management Parameters (2)
Sensor Management Parameters (2)
Default	Description	Parameter
false	Whether or not this observation should be used to mark obstacles	<source_name>/marking
0.0	How long to keep each sensor reading in seconds. A value of 0.0 will only keep the most recent reading.	<source_name>/observation_persistence
0.0	The minimum height in meters of a sensor reading considered valid. This is usually set to be at ground height, but can be set higher or lower based on the noise model of your sensor.	<source_name>/min_obstacle_height
2.0	The maximum height in meters of a sensor reading considered valid. This is usually set to be slightly higher than the height of the robot.	<source_name>/max_obstacle_height

---
Map Type Parameters
Map Type Parameters
Default	Description	Parameter
"voxel"	What map type to use. "voxel" or "costmap" are the supported types, with the difference between them being a 3D-view of the world vs. a 2D-view of the world.	map_type
0.0	The z origin of the map in meters	origin_z
0.2	The z resolution of the map in meters/cell	z_resolution
10	The number of voxels to in each vertical column, the height of the grid is z_resolution * z_voxels	z_voxels
z_voxels	The number of unknown cells allowed in a column considered to be "known"	unknown_threshold
0	The maximum number of marked cells allowed in a column considered to be "free"	mark_threshold

---
Map Management Parameters
Map Management Parameters
Default	Description	Parameter
true	Whether or not to use the static map to initialize the costmap. If the rolling_window parameter is set to true, this parameter must be set to false.	static_map
false	Whether or not to use a rolling window version of the costmap. If the static_map parameter is set to true, this parameter must be set to false.	rolling_window
0	The value for which a cost should be considered unknown when reading in a map from the map server. A value of zero results in this parameter being unused.	unknown_cost_value
100	The threshold value at which to consider a cost lethal when reading in a map from the map server	lethal_cost_threshold
"map"	The topic that the costmap subscribes to for the static map	map_topic

---
costmap_common_params.yaml (1)
costmap_common_params.yaml (1)
#This file contains common configuration options for the two costmaps used in the navigation stack for more details on the parameters in this file, and a full list of the parameters used by the costmaps, please see http://www.ros.org/wiki/costmap_2d
#For this example we'll configure the costmap in voxel-grid mode
map_type: voxel
#Voxel grid specific parameters
origin_z: 0.0
z_resolution: 0.2
z_voxels: 10
unknown_threshold: 9
mark_threshold: 0
#Set the tolerance we're willing to have for tf transforms
transform_tolerance: 0.3
#Obstacle marking parameters
obstacle_range: 2.5
max_obstacle_height: 2.0
raytrace_range: 3.0
#The footprint of the robot and associated padding
footprint: [[-0.325, -0.325], [-0.325, 0.325], [0.325, 0.325], [0.46, 0.0], [0.325, -0.325]]
footprint_padding: 0.01

---
costmap_common_params.yaml (2)
costmap_common_params.yaml (2)
#Cost function parameters
inflation_radius: 0.55
cost_scaling_factor: 10.0
#The cost at which a cell is considered an obstacle when a map is read from the map_server
lethal_cost_threshold: 100
#Configuration for the sensors that the costmap will use to update a map
observation_sources: base_scan
base_scan: {data_type: LaserScan, expected_update_rate: 0.4,
  observation_persistence: 0.0, marking: true, clearing: true, max_obstacle_height: 0.4, min_obstacle_height: 0.08}

---
global_costmap_params.yaml
global_costmap_params.yaml
#Independent settings for the global planner's costmap. Detailed descriptions of these parameters can be found at http://www.ros.org/wiki/costmap_2d
global_costmap:
  #Set the global and robot frames for the costmap
  global_frame: /map
  robot_base_frame: base_link
  #Set the update and publish frequency of the costmap
  update_frequency: 5.0
  publish_frequency: 0.0
  #We'll use a map served by the map_server to initialize this costmap
  static_map: true
  rolling_window: false
  footprint_padding: 0.02
Note: change publish_frequency to 5.0 to see the costmap

---
local_costmap_params.yaml
local_costmap_params.yaml
#Independent settings for the local planner's costmap. Detailed descriptions of these parameters can be found at http://www.ros.org/wiki/costmap_2d
local_costmap:
  #We'll publish the voxel grid used by this costmap
  publish_voxel_map: true
  #Set the global and robot frames for the costmap
  global_frame: odom
  robot_base_frame: base_link
  #Set the update and publish frequency of the costmap
  update_frequency: 5.0
  publish_frequency: 2.0
  #We'll configure this costmap to be a rolling window... meaning it is always
  #centered at the robot
  static_map: false
  rolling_window: true
  width: 6.0
  height: 6.0
  resolution: 0.025
  origin_x: 0.0
  origin_y: 0.0

---
Costmap_2d Subscriped Topics
Costmap_2d Subscriped Topics
Message Type	Description	Topic
	For each "PointCloud" source listed in the observation_sources parameter list, information from that source is used to update the costmap.	<point_cloud_topic>
	For each "LaserScan" source listed in the observation_sources parameter list, information from that source is used to update the costmap.	<laser_scan_topic>
	The costmap has the option of being initialized from a user-generated static map (see the static_map parameter). If this option is selected, the costmap makes a service call to the map_server to obtain this map.	"map"

---
Published Topics
Published Topics
Message Type	Description	Topic
	The occupied cells in the costmap	obstacles
nav_msgs/GridCells	The cells in the costmap that correspond to the occupied cells inflated by the inscribed radius of the robot	inflated_obstacles
	The unknown cells in the costmap	unknown_space
	Optionally advertised when the underlying occupancy grid uses voxels and the user requests the voxel grid be published.	voxel_grid
Note: In Hydro costmaps are published as Map (in Groovy they were GridCells).

---
move_base
move_base
- The move_base package lets you move a robot to desired positions using the navigation stack
- The move_base node links together a global and local planner to accomplish its global navigation task.
- The move_base node may optionally perform recovery behaviors when the robot perceives itself as stuck.

---
move_base Configuration File
move_base Configuration File
<launch>
<!--
  Example move_base configuration. Descriptions of parameters, as well as a full list of all amcl parameters, can be found at http://www.ros.org/wiki/move_base.
-->
  <node pkg="move_base" type="move_base" respawn="false" name="move_base_node" output="screen">
    <param name="footprint_padding" value="0.01" />
    <param name="controller_frequency" value="10.0" />
    <param name="controller_patience" value="3.0" />
    <param name="oscillation_timeout" value="30.0" />
    <param name="oscillation_distance" value="0.5" />
    <!--
    <param name="base_local_planner" value="dwa_local_planner/DWAPlannerROS" />
    -->
    <rosparam file="$(find navigation_stage)/move_base_config/costmap_common_params.yaml" command="load" ns="global_costmap" />
    <rosparam file="$(find navigation_stage)/move_base_config/costmap_common_params.yaml" command="load" ns="local_costmap" />
    <rosparam file="$(find navigation_stage)/move_base_config/local_costmap_params.yaml" command="load" />
    <rosparam file="$(find navigation_stage)/move_base_config/global_costmap_params.yaml" command="load" />
    <rosparam file="$(find navigation_stage)/move_base_config/base_local_planner_params.yaml" command="load" />
    <!--
    <rosparam file="$(find navigation_stage)/move_base_config/dwa_local_planner_params.yaml" command="load" />
    -->
  </node>
</launch>

---
Running ROS Navigation Stack in Stage
Running ROS Navigation Stack in Stage
Download the navigation tutorials from git
  - https://github.com/ros-planning/navigation_tutorials
The navigation_stage package holds example launch files for running the ROS navigation stack in stage
$ cd ~/ros/stacks
$ git clone https://github.com/ros-planning/navigation_tutorials.git

---
Running ROS Navigation Stack in Stage
Running ROS Navigation Stack in Stage
Description	Launch File
Example launch file for running the navigation stack with amcl at a map resolution of 5cm	launch/move_base_amcl_5cm
Example launch file for running the navigation stack with fake_localization at a map resolution of 10cm	launch/move_base_fake_localization_10cm.launch
Example launch file for running the navigation stack with multiple robots in stage.	launch/move_base_multi_robot.launch
Example launch file for running the navigation stack with gmapping at a map resolution of 5cm	launch/move_base_gmapping_5cm.launch

---
move_base_amcl_5cm.launch
move_base_amcl_5cm.launch
<launch>
  <master auto="start"/>
  <param name="/use_sim_time" value="true"/>
  <include file="$(find navigation_stage)/move_base_config/move_base.xml"/>
  <node name="map_server" pkg="map_server" type="map_server" args="$(find navigation_stage)/stage_config/maps/willow-full-0.05.pgm 0.05" respawn="false" />
  <node pkg="stage_ros" type="stageros" name="stageros" args="$(find navigation_stage)/stage_config/worlds/willow-pr2-5cm.world" respawn="false" >
    <param name="base_watchdog_timeout" value="0.2"/>
  </node>
  <include file="$(find navigation_stage)/move_base_config/amcl_node.xml"/>
  <node name="rviz" pkg="rviz" type="rviz" args="-d $(find navigation_stage)/single_robot.rviz" />
</launch>
To run this launch file type:
$ cd ~/ros/stacks/navigation_tutorials/navigation_stage/launch
$ roslaunch move_base_amcl_5cm.launch

---
Running the Launch File
Running the Launch File

---
move_base_gmapping_5cm.launch
move_base_gmapping_5cm.launch
<launch>
  <master auto="start"/>
  <param name="/use_sim_time" value="true"/>
  <include file="$(find navigation_stage)/move_base_config/move_base.xml"/>
  <node pkg="stage_ros" type="stageros" name="stageros" args="$(find navigation_stage)/stage_config/worlds/willow-pr2-5cm.world" respawn="false" >
    <param name="base_watchdog_timeout" value="0.2"/>
  </node>
  <include file="$(find navigation_stage)/move_base_config/slam_gmapping.xml"/>
  <node name="rviz" pkg="rviz" type="rviz" args="-d $(find navigation_stage)/single_robot.rviz" />
</launch>
To run this launch file type:
$ cd ~/ros/stacks/navigation_tutorials/navigation_stage/launch
$ roslaunch move_base_gmapping_5cm.launch

---
Using rviz with Navigation Stack
Using rviz with Navigation Stack
You can setup rviz to work with the navigation stack. This includes:
  - Setting the pose of the robot for a localization system like amcl
  - Displaying all the visualization information that the navigation stack provides
  - Sending goals to the navigation stack with rviz.

---
Robot Footprint
Robot Footprint
- It shows the footprint of the robot
- In our case, the robot has a pentagon-shape.
  - This parameter is configured in the costmap_common_params file.
- Topic: move_base_node/local_costmap/footprint_layer/footprint_stamped
- Type: geometry_msgs/PolygonStamped

---
Robot Footprint
Robot Footprint

---
Robot Footprint
Robot Footprint

---
2D Pose Estimate
2D Pose Estimate
- The 2D pose estimate (P shortcut) allows the user to initialize the localization system used by the navigation stack by setting the pose of the robot in the world.
- The navigation stack waits for the new pose of a new topic with the name initialpose.
- Click on the 2D Pose Estimate button and click on the map to indicate the initial position of your robot.
  - If you don't do this at the beginning, the robot will start the auto-localization process and try to set an initial pose.
- Note: For the "2d Nav Goal" and "2D Pose Estimate" buttons to work, the Fixed Frame must be set to "map".

---
2D Pose Estimate
2D Pose Estimate

---
2D Nav Goal
2D Nav Goal
- The 2D nav goal (G shortcut) allows the user to send a goal to the navigation by setting a desired pose for the robot to achieve.
- Click on the 2D Nav Goal button and select the map and the goal for your robot.
- You can select the x and y position and the end orientation for the robot.

---
2D Nav Goal
2D Nav Goal

---
Robot Moves to Destination
Robot Moves to Destination

---
Final Pose
Final Pose

---
Current Goal
Current Goal
- To show the goal pose that the navigation stack is attempting to achieve add a Pose Display
- Set its topic to /move_base_simple/goal
- You can see the goal pose as a red arrow
- It can be used to know the final position of the robot

---
Current Goal
Current Goal

---
Costmap
Costmap
- To see the costmap in rviz add a Map display
- To see the local costmap set the topic to:
/move_base_node/local_costmap/costmap
To see the global costmap set the topic to:
/move_base_node/global_costmap/costmap

---
Local Costmap
Local Costmap

---
Global Costmap
Global Costmap

---
Nodes Graph
Nodes Graph

---
Homework (not for submission)
Homework (not for submission)
- Install the navigation_stage package
- Test the different launch files in this package
- Send goals to the robot via rviz and examine the costmaps created
- Create a ROS node that prints the local costmap to the screen